## Slide 2
Project Overview
80 kg Autonomous Precision Agricultural Spraying UAV
This project presents the conceptual design of a heavy-lift quadcopter developed for autonomous crop spraying over large agricultural fields. The aircraft combines high payload capacity with precise navigation, controlled spray delivery, and automated mission execution.
Main Goals
Improve spray consistency and field coverage
Reduce operator workload and chemical exposure
Support repeatable autonomous spraying missions
Integrate flight, navigation, power, and spraying into one system
Design Focus:
Precision • Efficiency • Safety • Autonomy

## Slide 3
Mission & Design Objectives
Mission
  The UAV is designed to carry a liquid spray payload while following a planned route across agricultural fields. During the mission, it must maintain stable flight, accurate positioning, and controlled spray output while the operator supervises the system.
  Main Objectives
  Precision — Follow planned paths and maintain consistent coverage
  Efficiency — Reduce unnecessary overlap, time, and spray use
  Stability — Maintain controlled flight under high payload conditions
  Safety — Monitor aircraft status and respond to system faults
  Mission Flow;
    Plan Mission → Take Off → Navigate → Spray → Return → Land

## Slide 4
Design Requirements
Design Chain
Mission → Mass → Propulsion → Power→ Control → Spraying
Key Design Parameters
The aircraft requirements were derived from the intended agricultural mission and used as the basis for the engineering design. These values drive the sizing of the airframe, propulsion, power, avionics, and spraying systems.

## Slide 5
Overall UAV Concept
Quad-X Configuration
The selected X-frame layout places four propulsion units symmetrically around a central body. The payload, batteries, and major electronics are arranged around the center of gravity to support stable flight and balanced mass distribution.
Main Elements
Structural frame
Four propulsion units
Central spray tank
Battery and power system
Flight-control electronics
Navigation sensors
Spray boom and nozzles
System Concept
Navigation → Flight Controller → Propulsion Tank → Pump → Boom → Nozzles

## Slide 6
Propulsion System
Heavy-Lift Propulsion
At an MTOW of approximately 80 kg, the propulsion system must generate sufficient total thrust while retaining a practical thrust margin. The propulsion sizing was therefore based on rotor thrust, propeller operating conditions, motor power, and hover requirements.
Design Specifications
Configuration: 4 rotors
Operating condition: Hover + forward flight
Design point: Full aircraft mass
Sizing basis: Required thrust + safety margin
Propeller selection: Based on the calculated operating point
Motor selection: Matched to required thrust and power
Sizing Process
80 kg Aircraft → Required Thrust → Rotor Sizing → Motor → Propeller

## Slide 7
Power & Energy System
Balancing Power and Mass
The propulsion system creates the largest electrical demand, while avionics, sensors, and spraying equipment add additional loads. The selected dual-LiPo battery system of approximately 8 kg was incorporated into the aircraft mass and power budget.
Power Architecture
Dual LiPo → Power Distribution → ESCs → Motors Battery → Regulators → Avionics + Sensors + Spray System
Design Considerations
Propulsion power demand
Battery capacity
Battery mass
Peak current demand
Avionics power
Mission energy requirement
The battery selection therefore represents a compromise between energy availability, endurance, and aircraft mass.

## Slide 8
Flight Performance
Designed for Agricultural Flight
The UAV is optimized for controlled, low-speed agricultural operation rather than maximum speed. Maintaining stable altitude, attitude, and forward motion is important because aircraft movement directly affects spray coverage.
Performance Specifications
Operating Speed: 5–7 m/s
Spray Width: ~5.5–6 m
Maximum Takeoff Mass: ~80 kg
Payload: 55 L
Typical Mission
Takeoff → Transit → Spray Pass → Turn → Spray Pass → Return to home → Landing
The performance target prioritizes stable coverage and controlled operation over high-speed flight.

## Slide 9
Avionics System
The UAV's Control Centre
The avionics system connects the aircraft's sensors, navigation equipment, flight controller, propulsion system, and ground station. It processes information from the aircraft and turns mission commands into control actions.
Main Functions
Flight stabilization
Sensor processing
Navigation
Motor control
Autonomous mission execution
Telemetry
Failsafe management
Control Flow
Sensors → Flight Controller → ESCs → Motors Flight Controller → Telemetry → Ground Station

## Slide 10
Navigation & Autonomous Flight
RTK-GPS Based Navigation
The UAV uses RTK-GPS to improve positioning accuracy during autonomous waypoint missions. Navigation data is combined with onboard motion sensing so the flight controller can track the planned route and maintain stable aircraft motion.
Navigation Specifications
Navigation: RTK-GPS
Flight Mode: Autonomous waypoint navigation
Mission Planning: Predefined field routes
Control: Closed-loop position feedback
Autonomous Mission
Mission Planning → Waypoints → Position Estimation → Flight Control → Feedback
The operator supervises the mission while the aircraft handles continuous stabilization and waypoint tracking.

## Slide 11
Spraying System
20 L Liquid Delivery System
The spraying subsystem stores and delivers the agricultural liquid through a controlled pump, flow system, and nozzle arrangement. The tank is integrated near the aircraft's central region to limit changes in balance as the liquid is consumed.
Specifications
Tank Capacity: 55 L
Spray Width: ~5.5–6 m
System: Tank + Pump + Filter + Boom + Nozzles
Control: Regulated liquid delivery
Spray Flow
55 L Tank → Filter → Pump → Flow Control → Boom → Nozzles → Crop
The spraying system is integrated with the UAV's flight mission rather than operating independently.

## Slide 12
Precision Spraying
Connecting Flight With Spray Quality
Spray consistency depends on the relationship between aircraft motion and liquid delivery. Speed, altitude, flow rate, nozzle arrangement, and spray width must therefore be considered together.
Control Relationship
Flight Speed + Altitude + Flow Rate → Spray Coverage
The design targets a spray width of approximately 5.5–6 m, while stable flight helps maintain consistent distance between the nozzles and crop.
Goal
Uniform Coverage • Controlled Application • Minimum Unnecessary Overlap

## Slide 13
Safety and reliability
Safety by Design
An approximately 80 kg autonomous aircraft carrying a 55L liquid payload requires multiple layers of monitoring and failsafe protection. Abnormal conditions should trigger an appropriate response instead of allowing the aircraft to continue an unsafe mission.
Safety Functions
Battery monitoring
GPS/navigation monitoring
Communication monitoring
Return-to-home
Low-battery failsafe
Mission termination
Operator override
Pre-flight checks
Safety Logic
Fault Detected → Failsafe → Safe Flight Mode → Return / Land

## Slide 14
Data & Control Flow
A Closed-Loop Autonomous System
The aircraft continuously measures its actual condition and compares it with the desired mission state. The flight controller then adjusts the control commands to reduce errors and maintain the planned flight path.
Control Loop
Sensors → State Estimate → Flight Controller → Motor Commands → Aircraft Motion → Sensors
Mission Loop
Mission Plan → Waypoint Tracking → Position Feedback → Correction
This feedback structure allows the UAV to respond to disturbances instead of relying only on pre-programmed motor commands.

## Slide 15
Integrated 3D Design
Final Aircraft Concept
The final 3D model brings the structural frame, propulsion, payload, avionics, and spraying equipment together into one aircraft. This provides a practical visual check of how the different engineering decisions fit into the same physical platform.
Design Checks
Component interference
Propeller clearance
Tank placement
Spray-boom position
Ground clearance
Maintenance access
Overall proportions

## Slide 16
3D Design & Airframe Layout

## Slide 17
Simulation & Validation

## Slide 18
Results
What Does the Design Achieve?
The completed design brings the major engineering decisions together around the original agricultural mission. The preliminary analysis supports the feasibility of the proposed configuration while also showing where further physical validation is required.
Key Outcomes
~80 kg heavy-lift configuration established
55 L spray payload integrated
5–7 m/s operating range defined
~5.5–6 m spray width targeted
Dual-LiPo (~8 kg) power system incorporated
RTK-GPS autonomous navigation integrated
Propulsion sized around the full aircraft mass
Safety and monitoring functions included

## Slide 19
Conclusion
An Integrated Autonomous Spraying Platform
This project developed a conceptual ~80 kg autonomous agricultural spraying UAV by integrating the airframe, propulsion, power, avionics, navigation, spraying, and safety systems.
The key achievement is not simply the individual components, but their integration into one system designed around a real agricultural mission.
Final Mission
Carry Payload → Navigate Precisely → Spray Consistently → Monitor → Return Safely

## Slide 20
Student Name: Yodahe Leykun Assefa
Department: Aerospace Engineering
INSA 5th batch Student
ID: CTC-119-26
Year: 2026